## Slide 1: Ch. 2. BASICS of GEOCHEMICAL ANALYSIS
2-1. Classification (Types) of Chemical Analysis
  Qualitative analysis; determines the kinds of the constituents in the sample. Identifies the presence of the substance
  Quantitative analysis; determines not only kinds but also exact amounts of the constituents in the samples
  Wet/dry analysis; involves decomposition and other handlings using solutions or not
  Instrumental analysis; uses analytical instruments
  Destructive/nondestructive analysis; depends on whether the samples are destructed or not
  Trace analysis; analyzes specifically trace amount of constituents
  Isotopic analysis; analyzes isotopes
  Structural analysis; focusing on elucidate the internal structures of the samples
  Others; surface, bulk, sequential extraction, field, lab, spectroscopic, volumetric, gravimetric analyses, etc.

## Slide 2: Ch. 2. BASICS of GEOCHEMICAL ANALYSIS
2-2. Glossaries (Definition of Terms)
  2-2-1. Solutions & concentrations
    Solvent; dissolves
    Solute; being dissolved
    Solution; homogenized body of solvent + solute
    Molarity (M); conc. unit, mole # of solute in 1L solution
    Molality (m); conc. Unit, mole # of solute in 1kg solvent
    Normality (N); ditto, # of equivalents of silute in 1L solution
    Formality (F); ditto, # of moles of the combined sub. In 1L solution
    %; ditto, part per hundred
    %o; part per thousand
    Ppm, ppb, ppt; part per million, billion, trillion

## Slide 3: Ch. 2. BASICS of GEOCHEMICAL ANALYSIS
  2-2-2. Terms frequently used in Chem. Anal.
    Signal; analytical respond proportional to the amount of analytical objects (constituents)
    Backgrounds; a group of signals uncapable of providing analytical information
    Detection limit; the smallest signal distinguished from the backgrounds with enough confidence
    Sensitivity; the extent of signal respond upon a given amount of analytical object. Closely related to the DL
    Precision; reproducibility of results (signals)
    Accuracy; nearness of the measurements to the accepted (true) value
    Standard; samples used for the calibration of the signals (for the same analytical method)
    Reference material; used for checking the accuracy of the method
    Aliquot; a part of the sample used for analysis
    Significant figures; those figures (digits) meaningful (with certainty)

## Slide 4: Ch. 2. BASICS of GEOCHEMICAL ANALYSIS
Fig. 2-1. The red spectrum shows excitation with alpha particles (PIXE) and x rays (XRF). Excitation with only x rays is seen in the blue spectrum. From http://mynasa.nasa.gov/vision/universe/solarsystem/mars_history.html

## Slide 5: Ch. 2. BASICS of GEOCHEMICAL ANALYSIS
2-3. Statistical Evaluation of the Analytical Data
  Analytical errors are inevitable. Statistics for the evaluation of these errors
  PURPOSES of Statistical Evaluation:
    Estimation of closeness to the true value.
    Comparison of two different analytical data sets
    Decision of data rejection
    Error range estimation for the average with a certain confidence level.
    Appropriate report of the analytical results

## Slide 6
  2-3-1. Errors
    2-3-1-1. Determinate errors (having known causes) – This is the error should be eliminated. Caused by
      Analyzer (the person)
      Instrument
      Method
      How to find DE?
      Repeat analysis
      Analysis by another person with the same method
      Analysis of the reference material
      Blank test
      Analysis with the same method, but with different amount of sample
      Internal standard addition
      Check of the exp. Log & all the calculations

## Slide 7
  2-3-1. Errors
    2-3-1-2. Indeterminate or random errors (w/o certain causes, unknown causes)
      Cannot be eliminated. Always there!
      Can be (statistically) estimated only w/ repetition of the analysis (at least 3 times?)
      Reporting as an interval w/ a confidence level (significance level)
      Characteristics;
        Relatively small
        Equal probability of both negative and positive errors
        Error magnitude frequency of normal (Gaussian) distribution.

## Slide 8
  2-3-1. Errors
    2-3-1-2. Indeterminate errors
      2-3-1-2-1. Normal distribution (Gaussian distribution)

## Slide 9
  2-3-1. Errors
    2-3-1-2. Indeterminate errors
      2-3-1-2-2. Expressions of the indeterminate errors
        Range: xmax - xmin
        Relative range: Range/average * 100 (%)
        Average deviation from the mean:
        Standard deviation:
        Relative standard deviation:
        Confidence limit:
        For known true value
        For a single measurement-
        For multiple measurements-
        For unknown true value
        For a single measurement-
        For multiple measurements-

## Slide 10
  2-3-1. Errors
    2-3-1-2. Indeterminate errors
      2-3-1-2-2. Expressions of the indeterminate errors
        You are going to primarily use the following equations

## Slide 11
Z values corresponding to confidence levels
Confidence level (%) | Z
50.0 | 0.674
68.3 | 1.000
90.0 | 1.645
95.0 | 1.960
95.5 | 2.000
99.0 | 2.576
99.7 | 3.000
99.9 | 3.200

## Slide 12
t values corresponding to degree of freedom & confidence levels
Degree of Freedom | Confidence level |  |  |  | 
 | 80 | 90 | 95 | 99 | 99.9
1 | 3.08 | 6.31 | 12.7 | 63.7 | 637
2 | 1.89 | 2.92 | 4.30 | 9.92 | 31.6
3 | 1.64 | 2.35 | 3.18 | 5.84 | 12.9
4 | 1.53 | 2.13 | 2.78 | 4.60 | 8.60
5 | 1.48 | 2.02 | 2.57 | 4.03 | 6.86
6 | 1.44 | 1.94 | 2.45 | 3.71 | 5.96
7 | 1.42 | 1.90 | 2.36 | 3.50 | 5.40

## Slide 13
  2-3-2. Q-Test
    For the decision of rejection of a value in question
    Q quotient calculation
    Qexp > Qcrt  rejection
    Otherwise, keep the value.

## Slide 14
Q critical values corresponding to the number of measurements and
& confidence levels
Number of Measurement | Qcrt |  | 
 | 90 | 96 | 99
3 | 0.94 | 0.98 | 0.99
4 | 0.76 | 0.85 | 0.93
5 | 0.64 | 0.73 | 0.82
6 | 0.56 | 0.64 | 0.74
7 | 0.51 | 0.59 | 0.68
8 | 0.47 | 0.54 | 0.63
9 | 0.44 | 0.51 | 0.60

## Slide 15
  2-3-2. F-Test
    Comparison of the precision between two data sets
    F quotient calculation
    Fexp < Fcrt  no significant difference in precision between two data sets

## Slide 16
Q critical values corresponding to the number of measurements and
& confidence levels
Degree of freedom (numerator) | Degree of freedom (denominator) |  |  |  | 
 | 2 | 3 | 4 | 5 | 6
2 | 19.00 | 19.16 | 19.25 | 19.30 | 19.33
3 | 9.55 | 9.28 | 9.12 | 9.01 | 8.94
4 | 6.94 | 6.59 | 6.39 | 6.26 | 6.16
5 | 5.79 | 5.41 | 5.19 | 5.05 | 4.95
6 | 5.14 | 4.76 | 4.53 | 4.39 | 4.28

## Slide 17: Ch. 2. BASICS of GEOCHEMICAL ANALYSIS
2-4. Lab Safety
  Know way to the emergency exit
  Read fire emergency manual / locate fire extinguisher
  Use first aids
  Be cautious all the times (Concentrate!)
  No food/beverage in Lab
  Wear appropriate clothes
  Wear gloves and gogles anytime (protect yourself!)
  Volatiles handled in a hood
  Wipe out any liquid on table immediately (never touch it !)
  Deposit wastes as directed

## Slide 18: Ch. 2. BASICS of GEOCHEMICAL ANALYSIS
2-5. Apparatuses & Instruments Frequently Used in a Lab

## Slide 19: Ch. 2. BASICS of GEOCHEMICAL ANALYSIS

## Slide 20: Ch. 2. BASICS of GEOCHEMICAL ANALYSIS

## Slide 21: Ch. 2. BASICS of GEOCHEMICAL ANALYSIS